Serial Buffer for Orienteering Radio SRR/TinyMesh communication

1. Background
  1. The serial Buffer is a new HW/SW component in the FIF TinyMesh box that interfaces one or two SRRs to the RadioCrafts Module.
  2. The Serial Buffer solves a problem with the SRR to the Radio Module data path: the SRR does not respond to the serial channel handshake signals, so the Radio Module cannot throttle data, and the arrival of two punches close in time can cause loss of data. The radio module forces pauses in the data transmission for compliance with regulations, and data arriving during the pause can be lost.
  3. The solution is a RaspberryPi Pico module, connectng to multiple SRR modules, buffering and combining the data streams to one TinyMesh radio module.
  4. The SerialBuffer in context:
    input queue (chars)
    Output queue
    (single punch)

    Rx UART1 Tx
    SRR0
    Radio
    SRR1

    input queue (chars)
    Output queue
    (single punch)

    Rx UART0 Tx

2. Dev Project:
  1. The IDE is Visual Studio Code on a RspberryPi RP400 minicomputer, connected to the Pico’s debug port. The RP400 is also used as a test station, simulating the SRR and the TinyMesh radio via two serial channels.
  2. The Pico code is in C for speed, the test program running on the RP400 is in Python.
  3. See https://www.mathaelectronics.com/raspberry-pi-pico-a-complete-guide/
  4. Based on the uart_advanced example
  5. Started a new workspace, pico-projects, copy of the pico-examples workspace
  6. The Pico code is derived from the uart_advanced example, but substituted the interrupt-driven UART R/W with a poll loop.
  7. The projects are located in a new workspace, pico-projects . Open this workspace folder in Visual Studio Code, then open the C and Py files from the VS Code file explorer. This seures that all include folders are accessible.

1. SerialBuffer SW structure
  1. Dual FIFO buffers in two layers: a large, byte-based input buffer, followed by a small package-based output buffer. The package buffers are multiplexed to the serial output UART, maintaining contiguous punches from both channels.
  2. The CTS and RTS GPIOs are enabled.
  3. CTS is available on GPIO16.
  4. RTS is available on GPIO17.
  5. For UART0 those GPIOs are set in mode ALT3. For UART1 those GPIOs are in mode ALT5.
  6. See page 102 of BCM2835 ARM Peripherals
  7. See https://raspberrypi.github.io/pico-sdk-doxygen/group__hardware__gpio.html#ga2af81373f9f5764ac1a5bd6097477530
  8. Only enabling the handshake for the Pico Tx, since we assume that the Rx must aways be ready.
  9. Uart reads and writes are poll based, in a single execution loop.
  10. Writes into the input queue are not monitored for content.
  11. Continuous reads from the main large buffers into a secondary single-package buffer. When a package buffer holds a complete punch, it is sent to the UART in a contiguous stream. The punch is defined by the header byte 0xD3 and the length in the LEN field.
  12. Any chars before the header are transmitted, in particular, the 0x2 (STX) byte that precedes the header in the new record format. If the STX byte is detected, the transmitted punch will also include the terminating 0x3 (ETX) char.
  13. No control of CRC is done.
  14. A state machine keeps track of the punches in each channel, collecting a complete punch in a queue before requiring ownership of the output UART and sending a complete punch. Note that the order of the punches between stations is not guaranteed.
  15. The state machine controlling each channel:
    Serial buffer states
  16. Visual indicator: The LED blinks 5 times on power on. Then it will turn ON on Rx, OFF on Tx
  17. Internal pull-ups are enabled on the Pico RXD inputs, to enable operation with a single SRR. Otherwise the RXD inputs pick up stray signals.

Connections:
Serial buffer inserted between SRR units and the TinyMesh radio module

RP400 function	RP400 pin	SRR function	SRR pin	Pico function	Pico pin	TinyMesh function	TinyMesh pin
DBG SWDIO	18	-	-	SWDIO	debug - SWDIO	-	-
DBG GND	20	-	-	GND	debug - GND	-	-
DBG CLK	22	-	-	CLK	debug - SWCLK	-	-
UART0 Rx	10	-	-	UART0 Tx (GP0)	1	RXD	2
UART0 Tx	8	(SRR0) Tx	2	UART0 Rx (GP1)	2	-
UART0 RTS	11	-		UART0 CTS, (GP2)	4	RTS (CTS?)	5 (6?)
UART2 Tx	27	(SRR1) Tx	2	UART1 Rx (GP4)	7	-
	-			UART 1 Tx (GP5)	6	-
UART2 Rx	28			-	(unused)	-
UART2 RTS	-
GND		GND	1	GND (signal)	3,8,13,18,23,28,33	GND	1
-	-			GND (Power)	38	GND
-	-	VCC	7	Power: VSYS, 2 - 5.5 V	39	VCC	7
-	-	-	-	-	-	CONFIG	4
						CTS	6

1. Test:
  1. The RP400 used as test machine
  2. A Python script "SerialTest" sends data packages, blocking the Rx channel to force filling the buffer. Then It reads the whole buffer, comparing the Rx data to an internal test buffer.
  3. various buffer levels are tested, ending with an overfilled buffer to force the test to fail, validating the test method.
  4. By default, the primary UART (UART0) is assigned to the Linux console. If you wish to use the primary UART for other purposes, you must reconfigure Raspberry Pi OS. This can be done by using raspi-config
  5. For 2-channel test, the RP400 UART2 is used, since it is identical to UART1, whereas UART1 is a reduced functionality type. UART2 is used to transmit half of the punches (randomised).
  6. In order to use UART2, add the following line to /boot/config.txt: dtoverlay=uart2. Then it can be accessed as /dev/ttyAMA1
  7. Timing check: The Idle loop time is approx 1uS. With a baud rate 38400, the max input load on two channels is a char every 130uS, leaving ample time for handling two RX and one TX channel.

RP400 pinout:

GPI #	Pin #	ALT0	ALT1	ALT2	ALT3	ALT4	ALT5
0		SDA0	SA5	PCLK	SPI3_CE0_N	TXD2	SDA6
1		SCL0	SA4	DE	SPI3_MISO	RXD2	SCL6
2		SDA1	SA3	LCD_VSYNC	SPI3_MOSI	CTS2	SDA3
3		SCL1	SA2	LCD_HSYNC	SPI3_SCLK	RTS2	SCL3
4		GPCLK0	SA1	DPI_D0	SPI4_CE0_N	TXD3	SDA3
5		GPCLK1	SAO	DPI_D1	SPI4_MISO	RXD3	SCL3
6		GPCLK2	SOE_N	DPI_D2	SPI4_MOSI	CTS3	SDA4
7		SPI0_CE1_N	SWE_N	DPI_D3	SPI4_SCLK	RTS3	SCL4
8		SPI0_CE0_N	SDO	DPI_D4	_	TXD4	SDA4
9		SPI0_MISO	SD1	DPI_D5	_	RXD4	SCL4
10		SPI0_MOSI	SD2	DPI_D6	_	CTS4	SDA5
11		SPI0_SCLK	SD3	DPI_D7	_	RTS4	SCL5
12		PWM0	SD4	DPI_D8	SPI5_CE0_N	TXD5	SDA5
13		PWM1	SD5	DPI_D9	SPI5_MISO	RXD5	SCL5
14		TXD0	SD6	DPI_D10	SPI5_MOSI	CTS5	TXD1
15		RXD0	SD7	DPI_D11	SPI5_SCLK	RTS5	RXD1
16		FL0	SD8	DPI_D12	CTS0	SPI1_CE2_N	CTS1
17		FL1	SD9	DPI_D13	RTS0	SPI1_CE1_N	RTS1
18		PCM_CLK	SD10	DPI_D14	SPI6_CE0_N	SPI1_CE0_N	PWM0
19		PCM_FS	SD11	DPI_D15	SPI6_MISO	SPI1_MISO	PWM1
20		PCM_DIN	SD12	DPI_D16	SPI6_MOSI	SPIl_MOSI	GPCLK0
21		PCM_DOUT	SD13	DPI_D17	SPI6_SCLK	SPI1_SCLK	GPCLK1
22		SD0_CLK	SD14	DPI_D18	SD1_CLK	ARM_TRST	SDA6
23		SD0_XMD	SD15	DPI_D19	SD1_CMD	ARM_RTCK	SCL6
24		SD0_DATO	SD16	DPI_D20	SD1_DAT0	ARM_TDO	SPI3_CE1_N
25		SD0_DAT1	SD17	DPI_D21	SD1_DAT1	ARM_TCK	SPI4_CE1_N
26		SD0_DAT2	TE0	DPI_D22	SD1_DAT2	ARM_TDI	SPI5_CE1_N
27		SD0_DAT3	TE1	DPI_D23	SD1_DAT3	ARM_TMS	SPI6_CE1_N

Pico pinout

Pico I/O

SRR Protocol
Message structure:

SIAC: 0xD3 - LEN - CNH - CNL - SIID3 - SIID2 - SIID1 - SIID0 - CNH/AM/PM -TH - TL - TSS - MODE - CNTR - CNTT - CRC1 - CRC0

Oskar: "\x02\xD3\x0D\x00\x2A\x00\x1F\x87\x68\x0A\x81\x03\xD0\x00\x01\x10\xF3\x65\x03"

Nr	Oskar	Siac
0	0x02	STX	Only in new formats
1	0xD3	D3	Header byte, constant
2	LEN	LEN	Always 0x0D = 13
3	0x00	CNH	Station ID
4	0x27	CNL
5	0x00	SIID3	Chip ID
6	0x00	SIID2
7	SI1	SIID1
8	SI0	SIID0
9	0x05	CNH/AM/PM	Time
10	0x5E	TH
11	0xB2	TL
12	0x59	TSS
13	0x00	MODE
14	0x0E	CNTR
15	0x68	CNTT
16	CRC1	CRC1	CRC
17	CRC0	CRC0	CRC
18	0x03	ETX	Only in new format